## Slide 1: Transport Layer Berkeley Socket API – TCP and UDP

## Slide 2: Berkeley Socket API
Berkeley UNIX Sockets API
  Abstraction for applications to send & receive data
  Applications create sockets that “plug into” network
  Applications write/read to/from sockets
  Implemented in the kernel
  Facilitates development of network applications
  Hides details of underlying protocols & mechanisms
Also in Windows, Linux, and other OS’s

## Slide 3: Communications through Sockets
Client
Server
descriptor
port number
descriptor
port number
Application references a
socket through a descriptor
Socket bound to a port number
Application 1
Socket
Socket interface
User
Kernel
Application 2
User
Kernel
Underlying communication protocols
Underlying communication protocols
Communications network
Socket
Socket interface

## Slide 4: Transport Protocols
Host computers run two transport protocols on top of IP to enable process-to-process communications
User Datagram Protocol (UDP) enables best-effort connectionless transfer of individual block of information
Transmission Control Protocol (TCP) enables connection-oriented reliable transfer of a stream of bytes
Two services though Sockets: connection-oriented and connection-less

## Slide 5
Connection-oriented (TCP)
First, setup connection between two peer application processes
Then, reliable bidirectional in-sequence transfer of byte stream (boundaries not preserved in transfer)
Multiple write/read between peer processes
Finally, connection release
Connectionless (UDP)
Immediate transfer of one block of information (boundaries preserved)
No setup overhead & delay
Destination address with each block
Send/receive to/from multiple peer processes
Best-effort service only
  Possible out-of-order
  Possible loss
Stream Mode of Service

## Slide 6: Client & Server Differences
Server
  Specifies well-known port # when creating socket
  May have multiple IP addresses (net interfaces)
  Waits passively for client requests
Client
  Assigned ephemeral port #
  Initiates communications with server
  Needs to know server’s IP address & port #
    DNS for URL & server well-known port #
  Server learns client’s address & port #

## Slide 7: Socket Calls for Connection-Oriented Mode
socket()
socket()
bind()
read()
close()
Data
Data
Server
Client
listen()
accept()
Blocks
write()
connect()
Connect negotiation
write()
read()
Server does Passive Open
socket call creates socket to listen for connection requests
Server specifies type: TCP (stream)
socket call returns: non-negative integer descriptor; or -1 if unsuccessful
close()

## Slide 8: Socket Calls for Connection-Oriented Mode
socket()
socket()
bind()
read()
close()
Data
Data
Server
Client
listen()
accept()
Blocks
write()
connect()
Connect negotiation
write()
read()
bind assigns local address & port # to socket with specified descriptor
Can wildcard IP address for multiple net interfaces
bind call returns: 0 (success); or -1 (failure)
Failure if port # already in use or if reuse option not set
close()

## Slide 9: Socket Calls for Connection-Oriented Mode
socket()
socket()
bind()
read()
close()
Data
Data
Server
Client
listen()
accept()
Blocks
write()
connect()
Connect negotiation
write()
read()
listen indicates to TCP readiness to receive connection requests for socket with given descriptor
Parameter specifies max number of requests that may be queued while waiting for server to accept them
listen call returns: 0 (success); or -1 (failure)
close()

## Slide 10
socket()
socket()
bind()
read()
close()
Data
Data
Server
Client
listen()
accept()
Blocks
write()
connect()
Connect negotiation
write()
read()
Server calls accept to accept incoming requests
accept blocks if queue is empty
close()

## Slide 11: Socket Calls for Connection-Oriented Mode
socket()
socket()
bind()
read()
close()
Data
Data
Server
Client
listen()
accept()
Blocks
write()
connect()
Connect negotiation
write()
read()
close()
Client does Active Open
socket call creates socket to connect to server
Client specifies type: TCP (stream)
socket call returns: non-negative integer descriptor; or -1 if unsuccessful

## Slide 12
socket()
socket()
bind()
read()
close()
Data
Data
Server
Client
listen()
accept()
Blocks
write()
connect()
Connect negotiation
write()
read()
close()
connect establishes a connection on the local socket with the specified descriptor to the specified remote address and port #
connect returns 0 if successful; -1 if unsuccessful
Note: connect initiates TCP three-way handshake

## Slide 13: Socket Calls for Connection-Oriented Mode
socket()
socket()
bind()
read()
close()
Data
Data
Server
Client
listen()
accept()
Blocks
write()
connect()
Connect negotiation
write()
read()
accept wakes with incoming connection request
accept fills client address & port # into address structure
accept call returns: descriptor of new connection socket (success); or -1 (failure)
Client & server use new socket for data transfer
Original socket continues to listen for new requests
close()
Socket Calls for Connection-Oriented Mode

## Slide 14
socket()
socket()
bind()
read()
close()
Data
Data
Server
Client
listen()
accept()
Blocks
write()
connect()
Connect negotiation
write()
read()
Data Transfer
Client or server call write to transmit data into a connected socket
write call returns: # bytes transferred (success); or -1 (failure); blocks until all data transferred
close()

## Slide 15
socket()
socket()
bind()
read()
close()
Data
Data
Server
Client
listen()
accept()
Blocks
write()
connect()
Connect negotiation
write()
read()
Data Transfer
Client or server call read to receive data from a connected socket
read specifies: socket descriptor; pointer to a buffer; amount of data
read call returns: # bytes read (success); or -1 (failure); blocks if no data arrives
close()
Note: write and read can be called multiple times to transfer byte streams in both directions

## Slide 16
socket()
socket()
bind()
read()
close()
Data
Data
Server
Client
listen()
accept()
Blocks
write()
connect()
Connect negotiation
write()
read()
Connection Termination
Client or server call close when socket is no longer needed
close specifies the socket descriptor
close call returns: 0 (success); or -1 (failure)
Note: close initiates TCP graceful close sequence
close()
Socket Calls for Connection-Oriented Mode

## Slide 17
Berkeley Socket API - UDP

## Slide 18: Stream Mode of Service
Connectionless (UDP)
Immediate transfer of one block of information (boundaries preserved)
No setup overhead & delay
Destination address with each block
Send/receive to/from multiple peer processes
Best-effort service only
  Possible out-of-order
  Possible loss

## Slide 19: Socket Calls for Connection-Less Mode
socket()
sendto()
socket()
recvfrom()
Data
Server
Client
bind()
Blocks until server receives data from client
recvfrom()
close()
close()
Data
sendto()
Server starts first
Socket call creates socket of type UDP (datagram)
socket call returns: descriptor; or -1 if unsuccessful
bind assigns local address & port # to socket with specified descriptor

## Slide 20: Socket Calls for Connection-Less Mode
socket()
sendto()
socket()
recvfrom()
Data
Server
Client
bind()
Blocks until server receives data from client
recvfrom()
close()
close()
Data
sendto()
recvfrom copies bytes received in specified socket into a specified location
recvfrom blocks until data arrives

## Slide 21: Socket Calls for Connection-Less Mode
sendto()
socket()
sendto()
socket()
recvfrom()
Data
Server
Client
bind()
Blocks until server receives data from client
recvfrom()
close()
close()
Data
Client started
socket creates socket of type UDP (datagram)
socket call returns: descriptor; or -1 if unsuccessful

## Slide 22
sendto()
socket()
sendto()
socket()
recvfrom()
Data
Server
Client
bind()
Blocks until server receives data from client
recvfrom()
close()
close()
Data
sendto transfer bytes in buffer to specified socket
sendto specifies: socket descriptor; pointer to a buffer; amount of data; flags to control transmission behavior; destination address & port #; length of destination address structure
sendto returns: # bytes sent; or -1 if unsuccessful

## Slide 23
socket()
sendto()
socket()
recvfrom()
Data
Server
Client
bind()
Blocks until server receives data from client
recvfrom()
close()
close()
Data
sendto()
recvfrom wakes when data arrives
recvfrom specifies: socket descriptor; pointer to a buffer to put data; max # bytes to put in buffer; control flags; copies: sender address & port #; length of sender address structure
recvfrom returns # bytes received or -1 (failure)
Note: recvfrom returns data from at most one send, i.e. from one datagram

## Slide 24: Socket Calls for Connection-Less Mode
socket()
sendto()
socket()
recvfrom()
Data
Server
Client
bind()
Blocks until server receives data from client
recvfrom()
close()
close()
Data
sendto()
Socket Close
Client or server call close when socket is no longer needed
close specifies the socket descriptor
close call returns: 0 (success); or -1 (failure)