## Slide 1: Network Models: OSI Reference Model-Part 1
These slides are partially based on slides assembled by B. A. Forouzan, with grateful acknowledgement of the many others who made their course materials freely available online.

## Slide 2: Outline
  Network model : Layered Architecture
  OSI model-Physical, Datalink, Network Layers

## Slide 3: Network Model: Layered Architecture
Network model describes the architecture, components, and design used to establish communication between the source and destination systems.
A communication system is a complex piece of hardware and software.
A single, complex, unstructured program with many interacting components is very difficult to test and modify.
To overcome such problem, the ISO has developed a layered approach.

## Slide 4: Network Model: Layered Architecture
  Elements:
    Service: It is a set of actions that a layer provides to the higher layer.
    Protocol: It defines a set of rules that a layer uses to exchange the information with peer entity.
    Interface: It is a way through which the message is transferred from one layer to another layer.
  There are 2 predominant models available based on layered approach.
    Open Systems Interconnection (OSI) Model
    Transmission Control Protocol/Internet Protocol (TCP/IP) Model

## Slide 5: Layered Architecture Example

## Slide 6
Layers of OSI Model
OSI model was developed by the International Organization for Standardization (ISO) in1984.
It is a reference model

## Slide 7
Layer n peer protocol
n
Entity
n
Entity
n-PDUs
OSI Unified View: Protocols
The processes at layer n are referred to as layer n entities
The machines at the same layer use a set of precise and unambiguous rules called the layer-n protocol.
Layer-n peer processes communicate by exchanging Protocol Data Units (PDUs)

## Slide 8
OSI Unified View: Services
Layer n+1 transfers information by invoking the services provided by layer n
Services are available at Service Access Points (SAP’s)
Each layer passes data & control information to the layer below it until the physical layer is reached and transfer occurs
The data passed to the layer below is called a Service Data Unit (SDU); SDU’s are encapsulated in PDU’s

## Slide 9
Layers, Services & Protocols
SDU
Trailer
Payload
header
SDU
PDU at layer n+1
Layer n
Layer n+1

## Slide 10: Interaction between the layers

## Slide 11: Exchange using OSI Model

## Slide 12: OSI Model: Physical Layer
  Physical layer transmits the individual bits from one node to another node.
  It establishes, maintains and deactivates the physical connection.
  Hub, Repeater, Modem, Cables are Physical Layer devices.
  Functions:
  Line Configuration: It defines the way how two or more devices can be connected physically.
  Data Transmission: It defines the transmission mode between two devices on the network.
  Topology: It defines the way how network devices are arranged.
  Signals: It determines the type of the signal used for transmitting the information.

## Slide 13: OSI Model: Physical Layer

## Slide 14: OSI Model: Data Link Layer
  Packet in Data Link layer is referred to as Frame.
  Responsible for the error-free and efficient communication between two or more devices.
  Provides unique identification of each device that resides on a local network.
  Switch & Bridge are Data Link Layer devices.
  It contains two sub-layers:
    Logical Link Control: Transfer the packets to the Network layer and provides flow control.
    Media Access Control: Provides link between the Logical Link Control layer and the network's physical layer and is used for transferring the packets over the network.

## Slide 15: OSI Model: Data Link Layer
  Functions:
  Framing: Conversion from raw bit stream into packets. Frame contains header, packets and trailer
  Physical Addressing: Providing address to source and destination device.
  Flow Control: Technique through which the constant data rate is maintained on both the sides so that no data get corrupted.
  Error Control: Error control is achieved by adding a calculated value CRC (Cyclic Redundancy Check)
  Access Control: Used to determine which device has control over the shared link at a given time.

## Slide 16: OSI Model: Data Link Layer

## Slide 17: OSI Model: Data Link Layer

## Slide 18: OSI Model: Data Link Layer
Example:
A node with physical address 10 sends a frame to a node with physical address 87. At the data link level this frame contains physical addresses in the header. The trailer usually contains extra bits needed for error detection

## Slide 19: OSI Model: Network Layer
  It manages logical addressing, tracks the location of devices on the network.
  It determines the best path to move data from source to the destination based on the network conditions, the priority of service, and other factors.
  Routers are used to provide the routing services within an internetwork.
  The protocols used to route the network traffic are IPv4 and Ipv6.

## Slide 20: OSI Model: Network Layer
  Functions:
  Internetworking: Provides a logical connection between different devices.
  Addressing: Source and destination address are added to the header of the frame to identify the device on the internet.
  Routing: It determines the best optimal path out of the multiple paths from source to the destination.
  Packetizing: Process of converting the upper layer data into packets using Internet protocol (IP).
  Congestion control

## Slide 21: OSI Model: Network Layer

## Slide 22: OSI Model: Network Layer

## Slide 23: OSI Model: Network Layer
  Example:
  We want to send data from a node with network address A and physical address 10, located on one LAN, to a node with a network address P and physical address 95, located on another LAN. Because the two devices are located on different networks, we cannot use physical addresses only; the physical addresses only have local influence. What we need here are universal addresses (network/logical address) that can pass through the LAN boundaries.

## Slide 24: Q1
Which of following operates primarily at Layer 2 of the OSI model ?
  Hubs
  Switches
  Routers
  Repeaters

## Slide 25: Q2. What is the proper name for a "chunk" of information transmitted as a single unit at any layer of the OSI model?
Frame
Message Transmission Unit
Payload
Protocol Data Unit