## Slide 1: MODULE-2 DESIGN OF COMBINATIONAL LOGIC CIRCUITS
Bennett University
CSET105 – DIGITAL DESIGN

## Slide 2
MODULE-4
CSET-105: Digital Design
2
MODULE- 2
Design of Combinational Logic Circuits
Design Procedure, Binary Adder-Subtractor, Parallel Adder, Binary Multiplier, MagnitudeComparator-4 bit, Decoders, Encoders, Multiplexers, De-multiplexer, Parity generator and checker. Application of Mux and Demux.

## Slide 3
INTRODUCTION TO COMBINATIONAL LOGIC CIRCUITS
CSET-105: Digital Design
3
MODULE- 2

## Slide 4
INTRODUCTION TO COMBINATIONAL LOGIC
The digital system consists of two types of circuits,
Combinational circuit:
  consists of logic gates
  output at any time is determined from the present combination of inputs.
Sequential circuit:
  comprises both logic gates and the state of storage elements such as flip-flops.
  The output of a sequential circuit depends not only on present value of inputs but also on past state of inputs.
CSET-105: Digital Design
4
MODULE- 2

## Slide 5
INTRODUCTION TO COMBINATIONAL LOGIC
A combinational circuit consists of input variables, logic gates, and output variables.
The logic gates accept signals from inputs and output signals are generated according to the logic circuits employed in it.
Binary information from the given data transforms to desired output data in this process.
Both input and output are obviously the binary signals, i.e., either logic 1 or logic 0.
CSET-105: Digital Design
6
MODULE- 2

## Slide 6
INTRODUCTION TO COMBINATIONAL LOGIC
Block diagram of a combinational logic circuit
CSET-105: Digital Design
7
MODULE- 2

## Slide 7
INTRODUCTION TO COMBINATIONAL LOGIC
For n number of input variables to a combinational circuit, 2n possible combinations of binary input states are possible.
For each possible combination, there is one and only one possible output combination.
A combinational logic circuit can be described by m Boolean functions and each output can be expressed in terms of n input variables.
CSET-105: Digital Design
8
MODULE- 2

## Slide 8
DESIGN
PROCEDURE
CSET-105: Digital Design
23
MODULE- 2

## Slide 9
DESIGN PROCEDURE
Any combinational circuit can be designed by the following steps of design procedure.
The problem statement.
Identify the number of input and output variables.
The input and output variables are assign with letter symbols.
Construction of a truth table for the given logic.
The simplified Boolean expression is obtained by any method of minimization—algebraic method, Karnaugh map method.
A logic diagram is realized from the simplified Boolean expression using logic gates.
CSET105: Digital Design
24
MODULE- 2

## Slide 10
DESIGN PROCEDURE
EXAMPLE-1:
Design a combinational circuits with three input variables that will produce a logic-1 output when more than one input variables are HIGH state.
Solution:
STEP1: The problem statement.
Design a combinational circuits with three input variables that will produce a logic-1 Output when more than one input variables are HIGH.
STEP2: Identify the input and output variables
No. of inputs required: 3
No. of output required: 1
CSET105: Digital Design
25
MODULE- 2

## Slide 11
DESIGN PROCEDURE
STEP3: The input & outputs are assign with letter symbols
Letter symbol for inputs: A, B, C
Letter symbol for output: Y
STEP4: Construction of a truth table for the given logic
CSET105: Digital Design
26
MODULE- 2

## Slide 12
DESIGN PROCEDURE
STEP5: obtain the simplified expression for output variable using K-map simplification
STEP6: A logic diagram is realized from the simplified Boolean expression using logic gates
0 | 0
0 | 1
1 | 1
0 | 1
AB
C
00
01
11
10
0
1
Y = (AB)+(AC)+(BC)
CSET105: Digital Design
27
MODULE- 2

## Slide 13
DESIGN PROCEDURE
EXERCISES
Design a circuit with 4 inputs that has outputs with a binary value equal to the number of inputs that are HIGH.
A logic circuit accepts two 3-bit numbers and generates a logic output only when the two 3-bit numbers applied to the circuit are equal. Design the logic circuit.
Design a logic circuit that will produce a 1 only when the number of 1’s in a set of four inputs variables, A, B, and C, D are even (i.e. an even parity checker).
CSET105: Digital Design
31
MODULE- 2

## Slide 14
BINARY
ADDER
CSET105: Digital Design
32
MODULE- 2

## Slide 15
BINARY ADDER
A half-adder is a combinational circuit that can be used to add two binary bits.
It has two inputs that represent the two bits to be added and two outputs, with one producing the SUM output and the other producing the CARRY.
HALF ADDER
Inputs |  | Outputs | 
A | B | Carry (C) | Sum (S)
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
TRUTH TABLE
BLOCK DIAGRAM
CSET105: Digital Design
33
MODULE- 2

## Slide 16
BINARY ADDER
HALF ADDER
The Boolean expressions for the SUM and CARRY outputs are given by the equations,
Sum, S = A’B+ AB’= AB
Carry, C = A . B
CSET105: Digital Design
34
MODULE- 2

## Slide 17
BINARY ADDER
The first one representing the SUM output is that of an EX-OR gate, the second one representing the CARRY output is that of an AND gate.
HALF ADDER
LOGIC DIAGRAM
CSET105: Digital Design
35
MODULE- 2

## Slide 18
BINARY ADDER
The full adder circuit overcomes the limitation of the half-adder, which can be used to add two bits only.
A full adder is a combinational circuit that forms the arithmetic sum of three input bits.
It consists of 3 inputs and 2 outputs. Two of the input variables, represent the significant bits to be added.
The third input represents carry from previous lower significant position.
FULL ADDER
CSET105: Digital Design
36
MODULE- 2

## Slide 19
BINARY ADDER
FULL ADDER
Inputs |  |  | Outputs | 
A | B | Cin | Sum (S) | Carry (Cout)
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
LOGIC DIAGRAM
TRUTH TABLE
CSET105: Digital Design
37
MODULE- 2

## Slide 20
BINARY ADDER
FULL ADDER
K-MAP
The Boolean expressions for the SUM and CARRY outputs are given by the equations,
Sum, S= A’B’Cin+ A’BC’in + AB’C’in + ABCin
Carry, Cout = AB+ ACin + BCin .
CSET105: Digital Design
38
MODULE- 2

## Slide 21
BINARY ADDER
FULL ADDER
The logic diagram for the above functions is shown as,
Implementation of full-adder in Sum of Products
CSET105: Digital Design
39
MODULE- 2

## Slide 22
BINARY ADDER
FULL ADDER
The logic diagram of the full adder can also be implemented with two half-adders and one OR gate.
The S output from the second half adder is the exclusive-OR of Cin and the output of the first half-adder, giving
Sum = A’BC’in + AB’C’in + ABCin + A’B’Cin .
= C’in (A’B+AB’) + Cin (AB+A’B’)
= C’in (A’B+AB’) + Cin (A’B+AB’)’
= Cin  (A’B+AB’)
= Cin  (A  B) [x  y = x’y+ xy’]
CSET105: Digital Design
40
MODULE- 2

## Slide 23
BINARY ADDER
FULL ADDER
Carry, Cout = AB+ ACin+ BCin.
= AB+ ACin+ BCin (A +A’)
= ABCin+ AB+ ACin+ A’BCin
= AB (Cin+1) + ACin+ A’BCin [Cin+1= 1]
= AB+ ACin+ A’BCin
= AB+ ACin (B+B’) + A’BCin
= ABCin+ AB+ A’BCin+ AB’Cin
= AB (Cin+1) + A’BCin+ AB’Cin [Cin+1= 1]
= AB+ A’BCin+ AB’Cin
= AB+ Cin (A’B+AB’)
CSET105: Digital Design
41
MODULE- 2

## Slide 24
BINARY ADDER
FULL ADDER
Implementation of full adder with two half-adders and an OR gate
CSET105: Digital Design
42
MODULE- 2

## Slide 25
BINARY
SUBTRACTOR
CSET105: Digital Design
43
MODULE- 2

## Slide 26
BINARY SUBTRACTOR
A half Subtractor is a combinational circuit that can be used to subtract one binary digit from another to produce a DIFFERENCE output and a BORROW output.
The BORROW output here specifies whether a ‘1’ has been borrowed to perform the subtraction.
HALF SUBTRACTOR
Block schematic of half Subtractor
CSET105: Digital Design
44
MODULE- 2

## Slide 27
BINARY SUBTRACTOR
The truth table of half Subtractor, showing all possible input combinations and the corresponding outputs are shown below.
HALF SUBTRACTOR
Input |  | Output | 
A | B | Difference (D) | Borrow (Bout)
0 | 0 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
CSET105: Digital Design
45
MODULE- 2

## Slide 28
BINARY SUBTRACTOR
K-map simplification for half Subtractor:
The Boolean expressions for the DIFFERENCE and BORROW outputs are given by the equations,
Difference, D = A’B+ AB’= A  B
Borrow, Bout = A’ . B
HALF SUBTRACTOR
CSET105: Digital Design
46
MODULE- 2

## Slide 29
BINARY SUBTRACTOR
HALF SUBTRACTOR
Logic Implementation of Half-Subtractor
CSET105: Digital Design
47
MODULE- 2

## Slide 30
BINARY SUBTRACTOR
Comparing a half Subtractor with a half-adder, we find that the expressions for the SUM and DIFFERENCE outputs are just the same.
The expression for BORROW in the case of the half-Subtractor is also similar to what we have for CARRY in the case of the half-adder.
If the input A i.e. the minuend is complemented, an AND gate can be used to implement the BORROW output.
HALF SUBTRACTOR
CSET105: Digital Design
48
MODULE- 2

## Slide 31
BINARY SUBTRACTOR
A full Subtractor performs subtraction operation on two bits, a minuend and a subtrahend, and also takes into consideration whether a ‘1’ has already been borrowed by the previous adjacent lower minuend bit or not.
As a result, there are three bits to be handled at the input of a full Subtractor, namely the two bits to be subtracted and a borrow bit designated as Bin.
FULL SUBTRACTOR
CSET105: Digital Design
49
MODULE- 2

## Slide 32
BINARY SUBTRACTOR
There are two outputs, namely the DIFFERENCE output D and the BORROW output Bo. The BORROW output bit tells whether the minuend bit needs to borrow a ‘1’ from the next possible higher minuend bit.
FULL SUBTRACTOR
Block schematic of full Subtractor
CSET105: Digital Design
50
MODULE- 2

## Slide 33
BINARY SUBTRACTOR
FULL SUBTRACTOR
Inputs |  |  | Outputs | 
A | B | Bin | Difference(D) | Borrow(Bout)
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1
Truth Table
CSET105: Digital Design
51
MODULE- 2

## Slide 34
BINARY SUBTRACTOR
K-map simplification for full Subtractor:
The Boolean expressions for the DIFFERENCE and BORROW outputs are given by the equations,
Difference, D = A’B’Bin+ A’BB’in + AB’B’in + ABBin
Borrow, Bout = A’B+ A’Cin + BBin .
FULL SUBTRACTOR
CSET105: Digital Design
52
MODULE- 2

## Slide 35
BINARY SUBTRACTOR
FULL SUBTRACTOR
Implementation of full Subtractor
CSET105: Digital Design
53
MODULE- 2

## Slide 36
BINARY SUBTRACTOR
The logic diagram of the full Subtractor can also be implemented with two half Subtractor and one OR gate.
The difference, D output from the second half Subtractor is the exclusive-OR of Bin and the output of the first half Subtractor, giving
Difference, D = A’BB’in + AB’B’in + ABBin + A’B’Bin .
= B’in (A’B+AB’) + Bin (AB+A’B’)
= B’in (A’B+AB’) + Bin (A’B+AB’)’ [(x’y+xy’)’= (xy+x’y’)]
= Bin  (A’B+AB’)
= Bin  (A  B) [x  y = x’y+ xy’]
FULL SUBTRACTOR
CSET105: Digital Design
54
MODULE- 2

## Slide 37
BINARY SUBTRACTOR
Borrow, Bout = A’B+ BBin+ A’Bin.
= A’B+ BBin+ A’Bin (B +B’)
= A’BBin+ A’B+ BBin+ A’B’Bin
= A’B (Bin+1) + BBin+ A’B’Bin [Bin+1= 1]
= A’B+ BBin+ A’B’Bin
= A’B+ BBin (A+A’) + A’B’Bin [A+A’= 1]
= A’BBin+ A’B+ ABBin+ A’B’Bin
= A’B (Bin+1) + ABBin+ A’B’Bin [Bin+1= 1]
= A’B+ ABBin+ A’B’Bin
= A’B+ Bin (AB+A’B’)
= A’B+ Bin (A’B+AB’)’ [(x’y+xy’)’=(xy+x’y’)]
FULL SUBTRACTOR
CSET105: Digital Design
55
MODULE- 2

## Slide 38
BINARY SUBTRACTOR
Therefore, we can implement full Subtractor using two half Subtractor and OR gate as,
FULL SUBTRACTOR
Implementation of full Subtractor with two half Subtractor and an OR gate
CSET105: Digital Design
56
MODULE- 2

## Slide 39
BINARY ADDER & SUBTRACTOR
Adders & Subtractors are wildly used in in computer’s ALU (Arithmetic logic unit) to compute addition as well as CPU (Central Processing unit) and GPU (Graphics Processing unit) for graphics applications to reduce the circuit complexity.
Adder and subtractor are basically used for performing arithmetical functions like addition, subtraction, multiplication and division in electronic calculators and digital instruments.
APPLICATIONS
CSET105: Digital Design
56
MODULE- 2

## Slide 40
BINARY ADDER & SUBTRACTOR
Microcontrollers use adders for arithmetic additions, PC (program counter) and timers.
It is also used in microprocessors to calculate address, table indices, increment and decrement operators and slimier operations
It is also used in networking and DSP (Digital signal processor) oriented system
APPLICATIONS
CSET105: Digital Design
56
MODULE- 2

## Slide 41
PARALLEL ADDER
CSET105: Digital Design
57
MODULE- 2

## Slide 42
PARALLEL ADDER
A single full adder is capable of adding two one bit numbers and an input carry. In order to add a binary number with more than one bit an additional full adders must be employed.
The n-bit parallel adder can be constructed using “n” number of full adder circuits in parallel.
The block diagram of n-bit parallel adder using number of full adder circuits connected in cascade i.e. the carry output of each adder is connected to the carry input of the next higher order adder is shown in figure.
CSET105: Digital Design
58
MODULE- 2

## Slide 43
PARALLEL ADDER
CSET105: Digital Design
59
MODULE- 2
n-bit parallel Adder

## Slide 44
PARALLEL ADDER
The 4-bit binary adder using full adder circuits is capable of adding two 4-bit numbers resulting in a 4-bit sum and a carry output as shown in figure below.
CSET105: Digital Design
60
MODULE- 2
4-bit binary parallel Adder

## Slide 45
PARALLEL ADDER
Since all the bits of augend and addend are fed into the adder circuits simultaneously and the additions in each position are taking place at the same time, this circuit is known as parallel adder.
Let the 4-bit words to be added be represented by, A3 A2 A1 A0= 1 1 1 1 and B3 B2 B1 B0= 0 0 1 1.
CSET105: Digital Design
61
MODULE- 2

## Slide 46
PARALLEL ADDER
CSET105: Digital Design
62
MODULE- 2
Logic diagram of 4-bit parallel adder

## Slide 47
PARALLEL ADDER
The bits are added with full adders, starting from the least significant position, to form the sum bit and carry bit.
The input carry C0 in the least significant position must be 0. The carry output of the lower order stage is connected to the carry input of the next higher order stage.
Hence this type of adder is called ripple-carry adder.
CSET105: Digital Design
63
MODULE- 2

## Slide 48
PARALLEL ADDER
In the least significant stage, A0, B0 and C0 (which is 0) are added resulting in sum S0 and carry C1. This carry C1 becomes the carry input to the second stage.
Similarly in the second stage, A1, B1 and C1 are added resulting in sum S1 and carry C2, in the third stage, A2, B2 and C2 are added resulting in sum S2 and carry C3, in the third stage, A3, B3 and C3 are added resulting in sum S3 and C4, which is the output carry.
Thus the circuit results in a sum (S3 S2 S1 S0) and a carry output (Cout).
CSET105: Digital Design
64
MODULE- 2

## Slide 49
BINARY
MULTIPLIER
CSET105: Digital Design
79
MODULE- 2

## Slide 50
BINARY MULTIPLIER
Multiplication of binary numbers is performed in the same way as in decimal numbers.
The multiplicand is multiplied by each bit of the multiplier starting from the least significant bit.
Each such multiplication forms a partial product. Such partial products are shifted one position to left.
The final product is obtained from the sum of partial products.
CSET105: Digital Design
80
MODULE- 2

## Slide 51
BINARY MULTIPLIER
Consider the multiplication of two 2-bit numbers. The multiplicand bits are B1 and B0, the multiplier bits are A1 and A0, and the product is P3, P2, P1 and P0.
The first partial product is formed by multiplying B0 by A1A0. The multiplication of two bits such as A0 and B0 produces a 1 if both bits are 1; otherwise, it produces a 0.
This is identical to an AND operation. Therefore the partial product can be implemented with AND gates as shown in the diagram.
CSET105: Digital Design
81
MODULE- 2
2-Bit by 2-Bit Multiplier

## Slide 52
BINARY MULTIPLIER
The second partial product is formed by multiplying A1 by B1B0 and shifted one position to the left. The two partial products are added with two half adder (HA) circuits.
CSET105: Digital Design
82
MODULE- 2
2-Bit by 2-Bit Multiplier

## Slide 53
BINARY MULTIPLIER
CSET105: Digital Design
83
MODULE- 2
2-Bit by 2-Bit Multiplier

## Slide 54
BINARY MULTIPLIER
Usually there are more bits in the partial products and it is necessary to use full adders to produce the sum of the partial products.
The least significant bit of the product does not have to go through an adder since it is formed by the output of the first AND gate.
A combinational circuit binary multiplier with more bits can be constructed in a similar fashion. A bit of the multiplier is ANDed with each bit of the multiplicand in as many levels as there are bits in the multiplier.
CSET105: Digital Design
84
MODULE- 2
2-Bit by 2-Bit Multiplier

## Slide 55
BINARY MULTIPLIER
The binary output in each level of AND gates are added with the partial product of the previous level to form a new partial product. The last level produces the final product result.
Consider a multiplier circuit that multiplies a binary number of four bits by a number of four bits.
Let the multiplicand be represented by B3, B2, B1, B0 and the multiplier by A3, A2, A1, and A0.
CSET105: Digital Design
85
MODULE- 2
4-Bit by 4-Bit Multiplier

## Slide 56
BINARY MULTIPLIER
Since 4x4 multiplication process we need 16 AND gates and three 4-bit parallel adders to produce a product of eight bits.
As shown in figure each shifted multiplicand which is multiplied by either 0 or 1 depending on the corresponding, multiplier bit is called partial product.
The final 8-bit product is obtained by adding all partial products.
CSET105: Digital Design
86
MODULE- 2
4-Bit by 4-Bit Multiplier

## Slide 57
BINARY MULTIPLIER
CSET105: Digital Design
87
MODULE- 2
4-Bit by 4-Bit Multiplier

## Slide 58
BINARY MULTIPLIER
The multiplication of B0 and A0 produces a 1 if both bits are 1; otherwise it produces 0. This is identical to AND gates operation. Therefore the partial products can be implemented with AND gates.
The 4-bit partial products are added using 4-bit parallel adder. During addition of first partial product three most significant bits of it are added to the second partial product.
As we take only three bits from the partial product, the fourth bit (MSB) is considered as 0.
CSET105: Digital Design
88
MODULE- 2
4-Bit by 4-Bit Multiplier

## Slide 59
BINARY MULTIPLIER
The three most significant bits and carry out of first partial sum are then added to the third partial product.
Finally the three most significant bits and carry out of second partial sum are added to the fourth partial product the carryout and third sum represents the five most significant bits of the product.
Least significant bits of first and second partial sum represent P1 and P2 respectively & product B0A0 represents P0.
CSET105: Digital Design
89
MODULE- 2
4-Bit by 4-Bit Multiplier

## Slide 60
BINARY MULTIPLIER
CSET105: Digital Design
90
MODULE- 2
4-Bit by 4-Bit Multiplier

## Slide 61
MAGNITUDE COMPARATOR
CSET105: Digital Design
126
MODULE- 2

## Slide 62
MAGNITUDE COMPARATOR
A magnitude comparator is a combinational circuit that compares two given numbers (A and B) and determines whether one is equal to, less than or greater than the other.
The output is in the form of three binary variables representing the conditions A = B, A>B and A<B, if A and B are the two numbers being compared.
CSET105: Digital Design
127
MODULE- 2
Block diagram of magnitude comparator

## Slide 63
MAGNITUDE COMPARATOR
CSET105: Digital Design
128
MODULE- 2
Truth Table
Inputs |  |  |  | Outputs |  | 
A1 | A0 | B1 | B0 | A>B | A=B | A<B
0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0
1 | 1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0 | 1 | 0
2-Bit Magnitude Comparator

## Slide 64
MAGNITUDE COMPARATOR
CSET105: Digital Design
129
MODULE- 2
K-Map Simplification
2-Bit Magnitude Comparator

## Slide 65
MAGNITUDE COMPARATOR
CSET105: Digital Design
130
MODULE- 2
Logic Diagram
2-Bit Magnitude Comparator

## Slide 66
MAGNITUDE COMPARATOR
Let us consider the two binary numbers A and B with four digits each. Write the coefficient of the numbers in descending order as,
A = A3A2A1A0
B = B3 B2 B1 B0
Each subscripted letter represents one of the digits in the number. It is observed from the bit contents of two numbers that A = B when A3 = B3, A2 = B2, A1 = B1 and A0 = B0.
CSET105: Digital Design
131
MODULE- 2
4-Bit Magnitude Comparator

## Slide 67
MAGNITUDE COMPARATOR
When the numbers are binary they possess the value of either 1 or 0, the equality relation of each pair can be expressed logically by the equivalence function as
Xi = Ai Bi + Ai ′ Bi ′ for i = 0, 1, 2, 3
Or, Xi = (A  B)′ Or, Xi ′ = A  B
Or, Xi = (Ai Bi ′ + Ai ′Bi )′
where, Xi =1 only if the pair of bits in position i are equal (i.e., if both are 1 or both are 0).
CSET105: Digital Design
132
MODULE- 2
4-Bit Magnitude Comparator

## Slide 68
MAGNITUDE COMPARATOR
To satisfy the equality condition of two numbers A and B, it is necessary that all Xi must be equal to logic 1. This indicates the AND operation of all Xi variables.
In other words, we can write the Boolean expression for two equal 4-bit numbers.
(A = B) = X3X2X1 X0. (where X = A xnor B)
The binary variable (A=B) is equal to 1 only if all pairs of digits of the two numbers are equal.
CSET105: Digital Design
133
MODULE- 2
4-Bit Magnitude Comparator

## Slide 69
MAGNITUDE COMPARATOR
To determine if A is greater than or less than B, we inspect the relative magnitudes of pairs of significant bits starting from the most significant bit.
If the two digits of the most significant position are equal, the next significant pair of digits is compared. The comparison process is continued until a pair of unequal digits is found.
It may be concluded that A>B, if the corresponding digit of A is 1 and B is 0. If the corresponding digit of A is 0 and B is 1, we conclude that A<B.
CSET105: Digital Design
134
MODULE- 2
4-Bit Magnitude Comparator

## Slide 70
MAGNITUDE COMPARATOR
In a 4-bit comparator the condition of A>B can be possible in the following four cases:
  If A3 = 1 and B3 = 0
  If A3 = B3 and A2 = 1 and B2 = 0
  If A3 = B3, A2 = B2 and A1 = 1 and B1 = 0
  If A3 = B3, A2 = B2, A1 = B1 and A0 = 1 and B0 = 0
  Similarly the condition for A<B can be possible in the following four cases:
  If A3 = 0 and B3 = 1
  If A3 = B3 and A2 = 0 and B2 = 1
  If A3 = B3, A2 = B2 and A1 = 0 and B1 = 1
  If A3 = B3, A2 = B2, A1 = B1 and A0 = 0 and B0 = 1
CSET105: Digital Design
134
MODULE- 2
4-Bit Magnitude Comparator

## Slide 71
MAGNITUDE COMPARATOR
CSET105: Digital Design
134
MODULE- 2
4-Bit Magnitude Comparator

## Slide 72
MAGNITUDE COMPARATOR
Therefore, we can derive the logical expression of such sequential comparison by,
(A>B) = A3B3′ +X3A2B2′ +X3X2A1B1′ +X3X2X1A0B0′
(A<B) = A3′B3 +X3A2′B2 +X3X2A1′B1 +X3X2X1A0′B0
The symbols (A>B) and (A<B) are binary output variables that are equal to 1 when A>B or A<B, respectively.
The gate implementation of the three output variables just derived is simpler than it seems because it involves a certain amount of repetition.
The unequal outputs can use the same gates that are needed to generate the equal output.
CSET105: Digital Design
135
MODULE- 2
4-Bit Magnitude Comparator

## Slide 73
MAGNITUDE COMPARATOR
CSET105: Digital Design
136
MODULE- 2
Block diagram of 4-Bit magnitude comparator (IC7485)

## Slide 74
MAGNITUDE COMPARATOR
CSET105: Digital Design
136
MODULE- 2
Logic diagram of 4-Bit magnitude comparator

## Slide 75
MAGNITUDE COMPARATOR
CSET105: Digital Design
136
MODULE- 2
Block diagram of 8-Bit magnitude comparator

## Slide 76
MAGNITUDE COMPARATOR
Comparators are used in central processing units (CPUs) and microcontrollers (ALU).
These are used in control applications in which the binary numbers representing physical variables such as temperature, position, etc. are compared with a reference value.
Comparators are also used as process controllers and for Servo motor control.
Analogue-to-Digital converters, (ADC)
CSET105: Digital Design
133
MODULE- 2
Applications of Magnitude Comparator

## Slide 77
MULTIPLEXERS
CSET105: Digital Design
148
MODULE- 2

## Slide 78
MULTIPLEXERS
A Multiplexer or MUX, is a combinational circuit with more than one input line, one output line and more than one selection line.
A multiplexer selects binary information present from one of many input lines, depending upon the logic status of the selection inputs, and routes it to the output line.
Normally, there are 2n input lines and n selection lines whose bit combinations determine which input is selected. The multiplexer is often labeled as MUX in block diagrams.
CSET105: Digital Design
149
MODULE- 2

## Slide 79
MULTIPLEXERS
A multiplexer is also called a data selector, since it selects one of many inputs and steers the binary information to the output line.
CSET105: Digital Design
150
MODULE- 2
Block diagram of Multiplexer

## Slide 80
MULTIPLEXERS
The 2:1 multiplexer acts like an electronic switch that selects one of the two sources.
The circuit has two data input lines, one output line and one selection line, S.
When S= 0, the upper AND gate is enabled and I0 has a path to the output.
When S=1, the lower AND gate is enabled and I1 has a path to the output.
CSET105: Digital Design
151
MODULE- 2
2:1 MUX

## Slide 81
MULTIPLEXERS
CSET105: Digital Design
152
MODULE- 2
2:1 MUX

## Slide 82
MULTIPLEXERS
A 4-to-1-line multiplexer has four (2n) input lines, two (n) select lines and one output line.
It is the multiplexer consisting of four input channels and information of one of the channels can be selected and transmitted to an output line according to the select inputs combinations.
Selection of one of the four input channel is possible by two selection inputs.
CSET105: Digital Design
153
MODULE- 2
4:1 MUX

## Slide 83
MULTIPLEXERS
Each of the four inputs I0 through I3, is applied to one input of AND gate. Selection lines S1 and S0 are decoded to select a particular AND gate.
The outputs of the AND gate are applied to a single OR gate that provides the 1-line output.
CSET105: Digital Design
154
MODULE- 2
4:1 MUX
Truth table

## Slide 84
MULTIPLEXERS
The data output is equal to I0 only if S1= 0 and S0= 0; Y= I0S1’S0’.
The data output is equal to I1 only if S1= 0 and S0= 1; Y= I1S1’S0.
The data output is equal to I2 only if S1= 1 and S0= 0; Y= I2S1S0’.
The data output is equal to I3 only if S1= 1 and S0= 1; Y= I3S1S0.
When these terms are ORed, the total expression for the data output is,
Y= I0S1’S0’+ I1S1’S0 +I2S1S0’+ I3S1S0.
CSET105: Digital Design
157
MODULE- 2
4:1 MUX

## Slide 85
MULTIPLEXERS
CSET105: Digital Design
155
MODULE- 2
4:1 MUX

## Slide 86
MULTIPLEXERS
To demonstrate the circuit operation, consider the case when S1S0= 10.
The AND gate associated with input I2 has two of its inputs equal to 1 and the third input connected to I2.
The other three AND gates have at least one input equal to 0, which makes their outputs equal to 0.
The OR output is now equal to the value of I2, providing a path from the selected input to the output.
CSET105: Digital Design
156
MODULE- 2
4:1 MUX

## Slide 87
MULTIPLEXERS
CSET105: Digital Design
158
MODULE- 2
8:1 MUX

## Slide 88
MULTIPLEXERS
Communication system –The efficiency of communication system can be increased considerably using multiplexer. Multiplexer allow the process of transmitting different type of data such as audio, video at the same time using a single transmission line.
Telephone network – In telephone network, multiple audio signals are integrated on a single line for transmission with the help of multiplexers. In this way, multiple audio signals can be isolated and eventually, the desire audio signals reach the intended recipients.
Transmission from the computer system of a satellite – Multiplexer can be used for the transmission of data signals from the computer system of a satellite or spacecraft to the ground system using the GPS (Global Positioning System) satellites.
CSET105: Digital Design
159
MODULE- 2
MUX APPLICATIONS

## Slide 89
MULTIPLEXERS
It is possible to expand the range of input for multiplexer beyond the available range in the integrated circuits.
This can be accomplished by interconnecting several multiplexers. For example two 8:1 mux can be used together to form a 16:1 mux and two 16:1 mux can be used to realize the 32:1 mux.
Even we can realize 32:1 mux can be realized with a smaller sized mux like 8:1 or 4:1 or 2:1 by properly assigning the selection lines to those mux circuits.
CSET105: Digital Design
160
MODULE- 2
MULTIPLEXERS TREE

## Slide 90
MULTIPLEXERS
CSET105: Digital Design
161
MODULE- 2
MULTIPLEXERS TREE
8:1 Mux using 4:1 & 2:1 MUX

## Slide 91
MULTIPLEXERS
Here, the number of selection lines require to implement 8:1 mux is 3 (S2,S1,S0). The select inputs S1 and S0 of both multiplexers provided to the selections lines of 4:1 mux i.e S1, S0. Whereas the S3 selection input of the second level 2:1 multiplexer is connected to S3 selection line.
So for S2 = 0, the upper multiplexer is selected and input lines d0 to d3 are selected according to the selected inputs and data is transmitted to an output through the OR gate. When S2 = 1, the lower multiplexer is activated and input lines d4 to d7 are selected according to the selected inputs.
CSET105: Digital Design
162
MODULE- 2
MULTIPLEXERS TREE

## Slide 92
MULTIPLEXERS
CSET105: Digital Design
163
MODULE- 2
MULTIPLEXERS TREE
16:1 Mux using 4:1 MUX

## Slide 93
MULTIPLEXERS
Example1: Implement the following boolean function using 8:1 mux, F (A, B, C) = ∑m (1, 3, 5, 6).
Solution:
Variables, n= 3 (A, B, C)
Select lines= 3 (S2, S1, S0)
Input lines = 23 = 8 (D0, D1, D2, D3, D4, D5, D6, D7)
The three variables A, B, C are applied to the selection lines.
The minterms to be included (1, 3, 5 and 7) are chosen by making their corresponding input lines equal to logic-1.
Minterms 0, 2, 4 and 7 are not included by making their input lines equal to logic-0.
CSET105: Digital Design
164
MODULE- 2
  Implementation of boolean function using MUX

## Slide 94
MULTIPLEXERS
CSET105: Digital Design
165
MODULE- 2
  Implementation of boolean function using MUX

## Slide 95
MULTIPLEXERS
Example2: Implement the following boolean function using 4:1 multiplexer, F (A, B, C) = ∑m (1, 3, 5, 6).
Solution:
Variables, n= 3 (A, B, C)
Select lines= n-1 = 2 (S1, S0)
2n-1 to MUX i.e., 22 to 1 = 4 to 1 MUX
Input lines= 2n-1 = 22 = 4 (D0, D1, D2, D3)
Implementation table:
Apply variables B and C to the select lines. The procedures for implementing the function are:
List the input of the multiplexer
List under them all the minterms in two rows as shown below.
CSET105: Digital Design
166
MODULE- 2
  Implementation of boolean function using MUX

## Slide 96
MULTIPLEXERS
The first half of the minterms is associated with A’ and the second half with A. The given function is implemented by encircling the minterms of the function and applying the following rules to find the values for the inputs of the multiplexer.
If both the minterms in the column are not circled, apply 0 to the corresponding input.
If both the minterms in the column are circled, apply 1 to the corresponding input.
If the bottom minterm is circled and the top is not circled, apply A to the input.
If the top minterm is circled and the bottom is not circled, apply A’ to the input.
CSET105: Digital Design
167
MODULE- 2
  Implementation of boolean function using MUX

## Slide 97
MULTIPLEXERS
CSET105: Digital Design
168
MODULE- 2
  Implementation of boolean function using MUX
Truth table
Implementation table
Mux implementation

## Slide 98
MULTIPLEXERS
CSET105: Digital Design
169
MODULE- 2
  Implementation of boolean function using MUX

## Slide 99
MULTIPLEXERS
CSET105: Digital Design
170
MODULE- 2
  Implementation of boolean function using MUX

## Slide 100
DEMULTIPLEXERS
CSET105: Digital Design
171
MODULE-4

## Slide 101
DEMULTIPLEXERS
Demultiplexer means one into many. Demultiplexing is the process of taking information from one input and transmitting the same over one of several outputs.
A demultiplexer is a combinational logic circuit that receives information on a single input and transmits the same information over one of several (2n) output lines.
CSET105: Digital Design
172
MODULE-4

## Slide 102
DEMULTIPLEXERS
The block diagram of a demultiplexer has one input signal, ‘n’ select signals and 2n output signals.
The select inputs determine to which output the data input will be connected.
As the serial data is changed to parallel data, i.e., the input caused to appear on one of the n output lines, the demultiplexer is also called a “data distributer” or a “serial-to-parallel converter”.
CSET105: Digital Design
173
MODULE-4

## Slide 103
DEMULTIPLEXERS
A 1-to-4 demultiplexer has a single input, Din, four outputs (Y0 to Y3) and two select inputs (S1 and S0).
The input variable Din has a path to all four outputs, but the input information is directed to only one of the output lines.
CSET105: Digital Design
174
MODULE-4
  1:4 DEMUX

## Slide 104
DEMULTIPLEXERS
CSET105: Digital Design
175
MODULE-4
  1:4 DEMUX
Din | S1 | S0 | Y0 | Y1 | Y2 | Y3
0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1
Truth table of 1-to-4 line Demultiplexer

## Slide 105
DEMULTIPLEXERS
From the truth table, it is clear that the data input, Din is connected to the output Y0, when S1= 0 and S0=0 and the data input is connected to output Y1 when S1=0 and S0=1.
Similarly, the data input is connected to output Y2 and Y3 when S1=1 and S0=0 and when S1=1 and S0=1, respectively.
Also, from the truth table, the expression for outputs can be written as follows,
Y0= S1’S0’Din Y1= S1’S0Din Y2= S1S0’Din Y3= S1S0Din
CSET105: Digital Design
176
MODULE-4
  1:4 DEMUX

## Slide 106
DEMULTIPLEXERS
CSET105: Digital Design
177
MODULE-4
  1:4 DEMUX
Logic diagram of 1-to-4 line demultiplexer

## Slide 107
DEMULTIPLEXERS
Now, using the above expressions, a 1-to-4 line demultiplexer can be implemented using four 3-input AND gates and two NOT gates.
Here, the input data line Din, is connected to all the AND gates.
The two select lines S1, S0 enable only one gate at a time and the data that appears on the input line passes through the selected gate to the associated output line.
CSET105: Digital Design
178
MODULE-4
  1:4 DEMUX

## Slide 108
DEMULTIPLEXERS
A 1-to-8 line demultiplexer has a single input, Din, eight outputs (Y0 to Y7) and three select inputs (S2, S1 and S0). It distributes one input line to eight output lines based on the select inputs.
CSET105: Digital Design
179
MODULE-4
  1:8 DEMUX
Din | S2 | S1 | S0 | Y7 | Y6 | Y5 | Y4 | Y3 | Y2 | Y1 | Y0
0 | x | x | x | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 109
DEMULTIPLEXERS
From the above truth table, it is clear that the data input is connected with one of the eight outputs based on the select inputs.
Now from this truth table, the expression for eight outputs can be written as follows:
Y0= S2’S1’S0’Din Y4= S2 S1’S0’Din
Y1= S2’S1’S0Din Y5= S2 S1’S0Din
Y2= S2’S1S0’Din Y6= S2 S1S0’Din
Y3= S2’S1S0Din Y7= S2S1S0Din
CSET105: Digital Design
180
MODULE-4
  1:8 DEMUX

## Slide 110
DEMULTIPLEXERS
Now using the above expressions, the logic diagram of a 1-to-8 demultiplexer can be drawn as shown.
Here, the single data line, Din is connected to all the eight AND gates, but only one of the eight AND gates will be enabled by the select input lines.
For example, if S2S1S0= 000, then only AND gate-0 will be enabled and thereby the data input, Din will appear at Y0. Similarly, the different combinations of the select inputs, the input Din will appear at the respective output.
CSET105: Digital Design
181
MODULE-4
  1:8 DEMUX

## Slide 111
DEMULTIPLEXERS
CSET105: Digital Design
182
MODULE-4
  1:8 DEMUX

## Slide 112
DEMULTIPLEXERS
Example: Design 1:8 demultiplexer using 1:4 & 1:2 DEMUX.
CSET105: Digital Design
183
MODULE-4
  DEMULTIPLEXERS TREE

## Slide 113
DEMULTIPLEXERS
Example1: Implement the following boolean function using 1:8 Demux. F (A, B, C) = ∑m (1, 3, 5, 6).
CSET105: Digital Design
184
MODULE-4
  IMPLEMENTATION OF BOOLEAN EXPRESSION USING DEMUX
Inputs |  |  | Outputs
A | B | C | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 114
DEMULTIPLEXERS
CSET105: Digital Design
185
MODULE-4
  IMPLEMENTATION OF BOOLEAN EXPRESSION USING DEMUX

## Slide 115
DEMULTIPLEXERS
Example2: Implement full subtractor using demux
CSET105: Digital Design
186
MODULE-4
  IMPLEMENTATION OF BOOLEAN EXPRESSION USING DEMUX
Inputs |  |  | Outputs | 
A | B | Bin | Difference(D) | Borrow(Bout)
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1

## Slide 116
DEMULTIPLEXERS
CSET105: Digital Design
187
MODULE-4
  IMPLEMENTATION OF BOOLEAN EXPRESSION USING DEMUX
Full Subtractor using 1:8 demux

## Slide 117
DECODERS
CSET105: Digital Design
188
MODULE-4

## Slide 118
DECODERS
A decoder is a combinational circuit that converts binary information from ‘n’ input lines to a maximum of ‘2n’ unique output lines.
The encoded information is presented as ‘n’ inputs producing ‘2n’ possible outputs. The 2n output values are from 0 through 2n-1.
A decoder is provided with enable inputs to activate decoded output based on data inputs. When any one enable input is unasserted, all outputs of decoder are disabled.
CSET105: Digital Design
189
MODULE-4

## Slide 119
DECODERS
CSET105: Digital Design
190
MODULE-4
Block diagram of decoders

## Slide 120
DECODERS
A binary decoder is used when it is necessary to activate exactly one of 2n outputs based on an n-bit input value.
Here the 2 inputs are decoded into 4 outputs, each output representing one of the minterms of the two input variables.
As shown in the truth table, if enable input is 1 (EN= 1) only one of the outputs (Y0 – Y3), is active for a given input.
CSET105: Digital Design
191
MODULE-4
2 : 4 Decoders

## Slide 121
DECODERS
CSET105: Digital Design
192
MODULE-4
2 : 4 Decoders
Inputs |  |  | Outputs |  |  | 
Enable | A | B | Y3 | Y2 | Y1 | Y0
0 | x | x | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0 | 0 | 0
Truth table

## Slide 122
DECODERS
CSET105: Digital Design
193
MODULE-4
2 : 4 Decoders
Logic Diagram

## Slide 123
DECODERS
A 3-to-8 line decoder has three inputs (A, B, C) and eight outputs (Y0- Y7). Based on the 3 inputs one of the eight outputs is selected.
This decoder is used for binary-to-octal conversion. The input variables may represent a binary number and the outputs will represent the eight digits in the octal number system.
The output line whose value is equal to 1 represents the minterm equivalent of the binary number presently available in the input lines.
CSET105: Digital Design
194
MODULE-4
3 : 8 Decoders

## Slide 124
DECODERS
CSET105: Digital Design
195
MODULE-4
3 : 8 Decoders
Inputs |  |  | Outputs |  |  |  |  |  |  | 
A | B | C | Y0 | Y1 | Y2 | Y3 | Y4 | Y5 | Y6 | Y7
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Truth table

## Slide 125
DECODERS
CSET105: Digital Design
196
MODULE-4
3 : 8 Decoders
Logic Diagram

## Slide 126
DECODERS
Instruction decoder is the part of the CPU
Memory address decoding
Decoder outputs can be used to drive a 7 segment display (TTL 74LS47)
Binary Decoders such as binary or BCD ,decimal or octal etc and commonly available decoder IC’s (TTL 74LS138 3-to-8 line binary decoder or the 74ALS154 4-to-16 line decoder)
CSET105: Digital Design
197
MODULE-4
Applications

## Slide 127
DECODERS
Example: Design a 4 to 16 line decoders using 2 to 4 line decoders
To implement 4:16 decoder we need five 2:4 line decoders.
Decoder-1 is used to enable one of the decoder 2, 3, 4 and 5. Inputs of the first decoders are A and B i.e. MSB inputs of 4:16 decoders.
The inputs of decoders are connected together forming C and D inputs of 4:16 decoders.
When AB=00 decoder-1 is enabled, for AB=01 decoder-2 is enabled, for AB=10 decoder-3 is selected, and for AB=11 decoder-4 is enabled.
CSET105: Digital Design
198
MODULE-4
Cascading Decoders

## Slide 128
DECODERS
CSET105: Digital Design
199
MODULE-4
Cascading Decoders

## Slide 129
DECODERS
The combination of decoder and external logic gates can be used to implement single or multiple output function. The decoder can have one of the two output states either active or active high.
For active high output :
SOP function implementation
  When the decoder output is active high it generates minterms for input variables (i.e) it makes the selected output logic1. In such cases to implement the sop function we have to take sum of selected product terms generated by decoder. This can be implemented by ORing the selected decoder output.
CSET105: Digital Design
200
MODULE-4
Realization of Boolean Expression using Decoders

## Slide 130
DECODERS
CSET105: Digital Design
201
MODULE-4
Realization of Boolean Expression using Decoders

## Slide 131
DECODERS
POS function implementation: When the decoder output is active high POS function in similar manner as per SOP function except function output is complemented. This can be achieved by connecting NOR gates instead of OR gates .
CSET105: Digital Design
202
MODULE-4
Realization of Boolean Expression using Decoders
Single output function implementation using decoder and gate

## Slide 132
ENCODERS
CSET105: Digital Design
203
MODULE-4

## Slide 133
ENCODERS
An encoder is a combinational circuit that converts binary information from 2n input lines to a maximum of ‘n’ unique output lines.
An encoder is a digital circuit that performs the inverse operation of a decoder. Hence, the opposite of the decoding process is called encoding. The general structure of encoder circuit is,
CSET105: Digital Design
204
MODULE-4

## Slide 134
ENCODERS
Generally, digital encoders produce outputs of 2-bit, 3-bit or 4-bit codes depending upon the number of data input lines.
An "n-bit" binary encoder has 2n input lines and n-bit output lines with common types that include 4-to-2, 8-to-3 and 16-to-4 line configurations.
The output lines of a digital encoder generate the binary equivalent of the input line whose value is equal to “1”.
CSET105: Digital Design
205
MODULE-4

## Slide 135
ENCODERS
CSET105: Digital Design
206
MODULE-4
4 to 2 Encoder

## Slide 136
ENCODERS
One of the main disadvantages of standard digital encoders is that they can generate the wrong output code when there is more than one input present at logic level "1".
For example, if we make inputs D1 and D2 HIGH at logic "1" both at the same time, the resulting output is neither at "01" or at "10" but it will be at "11" which is an output binary number that is different to the actual input present.
CSET105: Digital Design
207
MODULE-4
Priority Encoder

## Slide 137
ENCODERS
One simple way to overcome this problem is to "Priorities" the level of each input pin and if there was more than one input at logic level "1" the actual output code would only correspond to the input with the highest designated priority.
Then this type of digital encoder is known commonly as a Priority Encoder or P-encoder for short.
CSET105: Digital Design
205
MODULE-4
Priority Encoder

## Slide 138
ENCODERS
A priority encoder is an encoder circuit that includes the priority function.
In priority encoder, if two or more inputs are equal to 1 at the same time, the input having the highest priority will take precedence. The higher the subscript number, higher the priority of the input.
Input D3, has the highest priority. So, regardless of the values of the other inputs, when D3 is 1, the output for xy is 11. D2 has the next priority level. The output is 10, if D2= 1 provided D3= 0. The output for D1 is generated only if higher priority inputs are 0, and so on down the priority levels.
CSET105: Digital Design
209
MODULE-4
Priority Encoder

## Slide 139
ENCODERS
CSET105: Digital Design
210
MODULE-4
4 to 2 Priority Encoder

## Slide 140
ENCODERS
CSET105: Digital Design
211
MODULE-4
4 to 2 Priority Encoder

## Slide 141
ENCODERS
CSET105: Digital Design
212
MODULE-4
4 to 2 Priority Encoder
4-Input Priority Encoder

## Slide 142
ENCODERS
CSET105: Digital Design
213
MODULE-4
8 to 3 Priority Encoder

## Slide 143
ENCODERS
(i). Keyboard Encoder
Priority encoders can be used to reduce the number of wires needed in a particular circuits or application that have multiple inputs.
For example, assume that a microcomputer needs to read the 104 keys of a standard QWERTY keyboard where only one key would be pressed either “HIGH” or “LOW” at any one time.
One way would be to connect all 104 wires from the individual keys on the keyboard directly to the computers input but this would be impractical for a small home PC.
CSET105: Digital Design
214
MODULE-4
Encoder Applications

## Slide 144
ENCODERS
Another alternative and better way would be to interface the keyboard to the PC using a priority encoder.
The 104 individual buttons or keys could be encoded into a standard ASCII code of only 7-bits (0 to 127 decimal) to represent each key or character of the keyboard and then input as a much smaller 7-bit B.C.D code directly to the computer.
Keypad encoders such as the 74C923 20-key encoder are available to do just that.
CSET105: Digital Design
215
MODULE-4
Encoder Applications

## Slide 145
ENCODERS
(ii) Positional Encoders
Another more common application is in magnetic positional control as used on ships navigation or for robotic arm positioning etc.
Here for example, the angular or rotary position of a compass is converted into a digital code by a 74LS148 8-to-3 line priority encoder and input to the systems computer to provide navigational data and an example of a simple 8 position to 3-bit output compass encoder is shown below.
Magnets and reed switches could be used at each compass point to indicate the needles angular position.
CSET105: Digital Design
216
MODULE-4
Encoder Applications

## Slide 146
ENCODERS
CSET105: Digital Design
217
MODULE-4
Encoder Applications

## Slide 147
ENCODERS
CSET105: Digital Design
218
MODULE-4
Encoder Applications

## Slide 148
ENCODERS
(iii). Interrupt Requests
Priority Encoders used for detecting interrupts in microprocessor applications.
Here the microprocessor uses interrupts to allow peripheral devices such as the disk drive, scanner, mouse, or printer etc, to communicate with it.
But the microprocessor can only “talk” to one peripheral device at a time so needs some way of knowing when a particular peripheral device wants to communicate with it.
CSET105: Digital Design
219
MODULE-4
Encoder Applications

## Slide 149
ENCODERS
The processor does this by using “Interrupt Requests” or “IRQ” signals to assign priority to all the peripheral devices to ensure that the most important peripheral device is serviced first.
The order of importance of the devices will depend upon their connection to the priority encoder.
Because implementing such a system using priority encoders such as the standard 74LS148 priority encoder IC involves additional logic circuits, purpose built integrated circuits such as the 8259 Programmable Priority Interrupt Controller is available.
CSET105: Digital Design
220
MODULE-4
Encoder Applications

## Slide 150
ENCODERS
CSET105: Digital Design
221
MODULE-4
Encoder Applications

## Slide 151: THANK YOU