## Slide 1: MODULE-3 DESIGN OF SEQUENTIAL LOGIC CIRCUITS
Bennett University
ECE2003 – DIGITAL LOGIC DESIGN

## Slide 2
MODULE-6
CSET105 – DIGITAL DESIGN
2
MODULE-3
Design of Sequential Logic Circuits
Latches, Flip-Flops-SR, D, JK & T, Shift Registers-SISO, SIPO, PISO,PIPO, Design of synchronous sequential circuits- State table and state diagrams, Design of counters-Modulo-n, Johnson, Ring, Up/Down, Design of Mealy and Moore FSM -Sequence detection.

## Slide 3
INTRODUCTION TO SEQUENTIAL
LOGIC CIRCUITS
CSET105 – DIGITAL DESIGN
3
MODULE-3

## Slide 4
INTRODUCTION TO SEQUENTIAL LOGIC
CSET105 – DIGITAL DESIGN
4
MODULE-3
Classification of Digital Logic Circuits

## Slide 5
INTRODUCTION TO SEQUENTIAL LOGIC
Digital electronics is classified into combinational logic and sequential logic.
In combinational logic circuits, the outputs at any instant of time depend only on the input signals present at that time.
For a change in input, the output occurs immediately.
CSET105 – DIGITAL DESIGN
5
MODULE-3
Combinational Circuit- Block Diagram

## Slide 6
INTRODUCTION TO SEQUENTIAL LOGIC
There are many applications in which digital outputs are required to be generated in accordance with the sequence in which the input signals are received.
The requirement can’t be satisfied with combinational circuits.
In sequential logic circuits, it consists of combinational circuits to which storage elements are connected to form a feedback path.
The storage elements are devices capable of storing binary information either 1 or 0.
The information stored in the memory elements at any given time defines the present state of the sequential circuit.
CSET105 – DIGITAL DESIGN
6
MODULE-3

## Slide 7
INTRODUCTION TO SEQUENTIAL LOGIC
The present state and the external circuit determine the output and the next state of sequential circuits.
Thus in sequential circuits, the output variables depend not only on the present input variables but also on the past history of input variables.
CSET105 – DIGITAL DESIGN
7
MODULE-3
Sequential Circuit- Block Diagram

## Slide 8
INTRODUCTION TO SEQUENTIAL LOGIC
CSET105 – DIGITAL DESIGN
8
MODULE-3
Combinational vs Sequential Circuit
S.No | Combinational logic | Sequential logic
1 | The output variable, at all times depends on the combination of input variables. | The output variable depends not only on the present input but also depend upon the past history of inputs.
2 | Memory unit is not required | Memory unit is required to store the past history of input variables.
3 | Faster in speed | Slower than combinational circuits.
4 | Easy to design | Comparatively difficult to design.
5 | Eg. MUX, Decoder, Parallel adder | Eg. Counter, Shift Register, Serial adder

## Slide 9
LATCHES
CSET105 – DIGITAL DESIGN
9
MODULE-3

## Slide 10
LATCHES
Latches and Flip-Flops are the basic building blocks of the most sequential circuits.
Latches are used for a sequential device that checks all of its inputs continuously and changes its outputs accordingly at any time independent of clocking signal.
Enable signal is provided with the latch. When enable signal is active output changes occur as the input changes.
But when enable signal is not activated input changes do not affect the output.
Flip-Flop is used for a sequential device that normally samples its inputs and changes its outputs only at times determined by clocking signal.
CSET105 – DIGITAL DESIGN
10
MODULE-3

## Slide 11
LATCHES
The simplest type of latch is the set-reset (SR) latch. It can be constructed from either two NOR gates or two NAND gates.
The two NOR gates are cross-coupled so that the output of NOR gate 1 is connected to one of the inputs of NOR gate 2 and vice versa.
The latch has two outputs Q and Q’ and two inputs, set and reset.
Before going to analyze the SR latch, we recall that a logic 1 at any input of a NOR gate forces its output to a logic 0.
Let us understand the operation of this circuit for various input/ output possibilities.
CSET105 – DIGITAL DESIGN
11
MODULE-3
SR Latch using NOR

## Slide 12
LATCHES
CSET105 – DIGITAL DESIGN
12
MODULE-3
SR Latch using NOR

## Slide 13
LATCHES
Case 1: S= 0 and R= 0
(Initially, Q= 1 and Q’= 0)
CSET105 – DIGITAL DESIGN
13
MODULE-3
SR Latch using NOR
Case 1: S= 0 and R= 0
(Initially, Q= 0 and Q’= 1)

## Slide 14
LATCHES
Case 2: S= 0 and R= 1
CSET105 – DIGITAL DESIGN
14
MODULE-3
SR Latch using NOR
Case 3: S= 1 and R= 0

## Slide 15
LATCHES
Case 4: S= 1 and R= 1
When R and S both are at logic 1, they force the outputs of both NOR gates to the low state, i.e., (Q=0 and Q’=0).
So, we call this an indeterminate or prohibited state, and represent this condition in the truth table as an asterisk (*).
This condition also violates the basic definition of a latch that requires Q to be complement of Q’.
Thus in normal operation this condition must be avoided by making sure that 1’s are not applied to both the inputs simultaneously.
CSET105 – DIGITAL DESIGN
15
MODULE-3
SR Latch using NOR

## Slide 16
LATCHES
CSET105 – DIGITAL DESIGN
16
MODULE-3
SR Latch using NOR
S | R | Present state | Next state | State
 |  | Qn | Qn+1 | 
0 0 | 0 0 | 0 1 | 0 1 | No Change (NC)
0 0 | 1 1 | 0 1 | 0 0 | Reset
1 1 | 0 0 | 0 1 | 1 1 | Set
1 1 | 1 1 | 0 1 | x x | Indeterminate*
Truth table

## Slide 17
LATCHES
The SR latch can also be implemented using NAND gates. The inputs of this Latch are S and R.
To understand how this circuit functions, recall that a low on any input to a NAND gate forces its output high.
CSET105 – DIGITAL DESIGN
17
MODULE-3
SR Latch using NAND
Logic Symbol
SR latch using NAND gates

## Slide 18
LATCHES
CSET105 – DIGITAL DESIGN
18
MODULE-3
SR Latch using NAND
S | R | Qn | Qn+1 | State
0 0 | 0 0 | 0 1 | x x | Indeterminate*
0 0 | 1 1 | 0 1 | 1 1 | Set
1 1 | 0 0 | 0 1 | 0 0 | Reset
1 1 | 1 1 | 0 1 | 0 1 | No Change (NC)
Truth table

## Slide 19
LATCHES
In the SR latch, the output changes occur immediately after the input changes i.e, the latch is sensitive to its S and R inputs all the time.
A latch that is sensitive to the inputs only when an enable input is active. Such a latch with enable input is known as gated SR latch.
The circuit behaves like SR latch when EN= 1. It retains its previous state when EN= 0.
CSET105 – DIGITAL DESIGN
19
MODULE-3
Gated Latch using NAND

## Slide 20
LATCHES
CSET105 – DIGITAL DESIGN
20
MODULE-3
Gated Latch using NAND

## Slide 21
LATCHES
CSET105 – DIGITAL DESIGN
21
MODULE-3
Gated Latch using NAND
EN | S | R | Qn | Qn+1 | State
1 1 | 0 0 | 0 0 | 0 1 | 0 1 | No Change (NC)
1 1 | 0 0 | 1 1 | 0 1 | 0 0 | Reset
1 1 | 1 1 | 0 0 | 0 1 | 1 1 | Set
1 1 | 1 1 | 1 1 | 0 1 | x x | Indeterminate *
0 0 | x x | x x | 0 1 | 0 1 | No Change (NC)
Truth table

## Slide 22
LATCHES
CSET105 – DIGITAL DESIGN
22
MODULE-3
Gated Latch using NAND

## Slide 23
LATCHES
In SR latch, when both inputs are same (00 or 11), the output either does not change or it is invalid.
In many practical applications, these input conditions are not required.
These input conditions can be avoided by making them complement of each other.
Therefore, only two input conditions exists, either S=0 and R=1 or S=1 and R=0.
This modified SR latch is known as D latch.
CSET105 – DIGITAL DESIGN
23
MODULE-3
D - Latch using NAND

## Slide 24
LATCHES
CSET105 – DIGITAL DESIGN
24
MODULE-3
D - Latch using NAND

## Slide 25
LATCHES
CSET105 – DIGITAL DESIGN
25
MODULE-3
D - Latch using NAND
EN | D | Qn | Qn+1 | State
1 1 0 | 0 1 x | x x x | 0 1 Qn | Reset Set No Change (NC)
Truth table
Input and output waveforms

## Slide 26
FLIP-FLOPS
CSET105 – DIGITAL DESIGN
26
MODULE-3

## Slide 27
FLIP-FLOPS
The state of a Flip-Flop is switched by a momentary change in the input signal.
This momentary change is called a trigger and the transition it causes is said to trigger the Flip-Flop.
Clocked Flip-Flops are triggered by pulses. A clock pulse starts from an initial value of 0, goes momentarily to 1 and after a short time, returns to its initial 0 value.
Level Triggering: In the level triggering the output state is allowed to change according to inputs when active (either positive or negative) is maintained at the enable input.
Latches are controlled by enable signal, and they are level triggered, either positive level triggered or negative level triggered.
CSET105 – DIGITAL DESIGN
27
MODULE-3
Triggering of Flip flops

## Slide 28
FLIP-FLOPS
There are two types of level triggered latches:
  (i). Positive level triggered: The output of the latch responds to the input changes only when the enable input is 1(HIGH).
  (ii). Negative level triggered: The output of the latch responds to the input changes only when the enable input is 0 (LOW).
CSET105 – DIGITAL DESIGN
28
MODULE-3
Triggering of Flip flops

## Slide 29
FLIP-FLOPS
CSET105 – DIGITAL DESIGN
29
MODULE-3
Triggering of Flip flops

## Slide 30
FLIP-FLOPS
Edge Triggering: In the edge triggering the output responds to the changes in the input only at the positive or negative edges of the clock pulse at the clock input.
Flip-Flops are different from latches. Flip-Flops are pulse or clock edge triggered instead of level triggered.
(i). Positive edge triggering: Here the output responds to the changes in the input only at the positive edge of the clock pulse at the clock input.
CSET105 – DIGITAL DESIGN
30
MODULE-3
Triggering of Flip flops

## Slide 31
FLIP-FLOPS
(ii). Negative edge triggering: Here the output responds to the changes in the input only at the negative edge of the clock pulse at the clock input.
CSET105 – DIGITAL DESIGN
31
MODULE-3
Triggering of Flip flops

## Slide 32
FLIP-FLOPS
The basic 1-bit digital memory circuit is known as a flip-flop. Flip-Flops are synchronous bistable devices (has two outputs Q and Q’).
In this case, the term synchronous means that the output changes state only at a specified point on the triggering input called the clock (CLK), i.e., changes in the output occur in synchronization with the clock. It can have only two states, either the 1 state or the 0 state.
CSET105 – DIGITAL DESIGN
32
MODULE-3
Flip flops

## Slide 33
FLIP-FLOPS
Flip-flops can be obtained by using NAND or NOR gates.
If Q is 1 i.e., Set, then Q' is 0; if Q is 0 i.e., Reset, then Q' is 1. That means Q and Q' cannot be at the same state simultaneously.
There are different types of flip-flops depending on how their inputs and clock pulses cause transition between two states.
We will discuss four different types of flip-flops SR, D, JK, and T.
Basically D, J-K, and T are three different modifications of the S-R flip-flop.
CSET105 – DIGITAL DESIGN
33
MODULE-3
Flip flops

## Slide 34
FLIP-FLOPS
The S and R inputs of the S-R Flip-Flop are called synchronous inputs because data on these inputs are transferred to the Flip-Flop's output only on the triggering edge of the clock pulse.
The circuit is similar to SR latch except enable signal is replaced by clock pulse (CLK).
On the positive edge of the clock pulse, the circuit responds to the S and R inputs.
CSET105 – DIGITAL DESIGN
34
MODULE-3
SR Flip flops

## Slide 35
FLIP-FLOPS
When S is HIGH and R is LOW, the Q output goes HIGH on the triggering edge of the clock pulse, and the Flip-Flop is SET.
When S is LOW and R is HIGH, the Q output goes LOW on the triggering edge of the clock pulse, and the Flip-Flop is RESET.
When both S and R are LOW, the output does not change from its prior state.
An invalid condition exists when both S and R are HIGH.
CSET105 – DIGITAL DESIGN
35
MODULE-3
SR Flip flops

## Slide 36
FLIP-FLOPS
CSET105 – DIGITAL DESIGN
36
MODULE-3
SR Flip flops

## Slide 37
FLIP-FLOPS
CSET105 – DIGITAL DESIGN
37
MODULE-3
SR Flip flops

## Slide 38
FLIP-FLOPS
CSET105 – DIGITAL DESIGN
38
MODULE-3
SR Flip flops

## Slide 39
FLIP-FLOPS
CSET105 – DIGITAL DESIGN
39
MODULE-3
SR Flip flops

## Slide 40
FLIP-FLOPS
Like in D latch, in D Flip-Flop the basic SR Flip-Flop is used with complemented inputs.
The D Flip-Flop is similar to D-latch except clock pulse is used instead of enable input.
To eliminate the undesirable condition of the indeterminate state in the RS Flip-Flop is to ensure that inputs S and R are never equal to 1 at the same time. This is done by D Flip-Flop.
The D (delay or data) Flip-Flop has one input called delay input and clock pulse input.
CSET105 – DIGITAL DESIGN
40
MODULE-3
D Flip flops

## Slide 41
FLIP-FLOPS
CSET105 – DIGITAL DESIGN
41
MODULE-3
D Flip flops

## Slide 42
FLIP-FLOPS
CSET105 – DIGITAL DESIGN
42
MODULE-3
D Flip flops

## Slide 43
FLIP-FLOPS
CSET105 – DIGITAL DESIGN
43
D Flip flops

## Slide 44
FLIP-FLOPS
JK means Jack Kilby, Texas Instrument (TI) Engineer, who invented IC in 1958.
JK Flip-Flop has two inputs J(set) and K(reset). A JK Flip-Flop can be obtained from the clocked SR Flip-Flop by augmenting two AND gates.
The data input J and the output Q’ are applied to the first AND gate and its output (JQ’) is applied to the S input of SR Flip-Flop.
Similarly, the data input K and the output Q is applied to the second AND gate and its output (KQ) is applied to the R input of SR Flip-Flop.
CSET105 – DIGITAL DESIGN
44
JK Flip flops

## Slide 45
FLIP-FLOPS
CSET105 – DIGITAL DESIGN
45
JK Flip flops

## Slide 46
FLIP-FLOPS
Case1: J= K= 0
When J=K= 0, both AND gates are disabled. Therefore clock pulse have no effect, hence the Flip-Flop output is same as the previous output.
Case2: J= 0, K= 1
When J= 0 and K= 1, AND gate 1 is disabled i.e., S= 0 and R= 1. This condition will reset the Flip-Flop to 0.
Case3: J= 1, K= 0
When J= 1 and K= 0, AND gate 2 is disabled i.e., S= 1 and R= 0. Therefore the Flip-Flop will set on the application of a clock pulse.
Case4: J= K= 1
When J=K= 1, it is possible to set or reset the Flip-Flop. If Q is High, AND gate 2 passes on a reset pulse to the next clock. When Q is low, AND gate 1 passes on a set pulse to the next clock. Either way, Q changes to the complement of the last state i.e., toggle. Toggle means to switch to the opposite state.
CSET105 – DIGITAL DESIGN
46
JK Flip flops

## Slide 47
FLIP-FLOPS
The function of JK flip flop using SR flip flop and AND gate can also be performed by adding extra input terminal to input terminals of NAND gates. Figure (b) shows the modified circuit of JK flip flop which has only NAND gates.
CSET105 – DIGITAL DESIGN
47
JK Flip flops

## Slide 48
FLIP-FLOPS
CSET105 – DIGITAL DESIGN
48
JK Flip flops

## Slide 49
FLIP-FLOPS
CSET105 – DIGITAL DESIGN
49
JK Flip flops

## Slide 50
FLIP-FLOPS
CSET105 – DIGITAL DESIGN
50
JK Flip flops

## Slide 51
FLIP-FLOPS
The T (Toggle) Flip-Flop is a modification of the JK Flip-Flop. It is obtained from JK Flip-Flop by connecting both inputs J and K together, i.e., single input.
Regardless of the present state, the Flip-Flop complements its output when the clock pulse occurs while input T= 1.
CSET105 – DIGITAL DESIGN
51
T Flip flops

## Slide 52
FLIP-FLOPS
CSET105 – DIGITAL DESIGN
52
T Flip flops

## Slide 53
FLIP-FLOPS
CSET105 – DIGITAL DESIGN
53
T Flip flops

## Slide 54
FLIP-FLOPS
CSET105 – DIGITAL DESIGN
54
T Flip flops

## Slide 55
FLIP-FLOPS
CSET105 – DIGITAL DESIGN
55
Flip flops Summary